Practice – 20.3 Resistance and Resistivity

1.  What is the resistance of a 20.0-m-long piece of 12-gauge copper wire having a 2.053-mm diameter?  (Cu = 1.72 x 10-8 .m)

2.  The diameter of 0-gauge copper wire is 8.252 mm.  Find the resistance of a 1.00-km length of such wire used for power transmission.  (Cu = 1.72 x 10-8 .m)

3.  If the 0.100-mm diameter tungsten filament in a light bulb is to have a resistance of 0.200 , how long should it be?  (W = 5.6 x 10-8 .m)

4.  Find the ratio of the diameter of aluminum to copper wire, if they have the same resistance per unit length (as they might in household wiring).  (Cu = 1.72 x 10-8 .m and Al = 2.65 x 10-8 .m)

5.  What current flows through a 2.54-cm-diameter rod of pure silicon that is 20.0 cm long, when 1.00 × 103 V is applied to it?  (Such a rod may be used to make nuclear-particle detectors, for example.)  (Si = 2300 .m)

6.  A wire is drawn through a die, stretching it to four times its original length.  By what factor does its resistance increase?

Solutions:

1.  0.104         2.  0.322 3.  0.028 m        4.  1.24        5.  1.10 x 10-3 A        6.  16