Physics 200						Name:  ___________________________

Notes: Chapter Sections 20.3, 20.4, and 21.1

Notes – 20.3 Resistance and Resistivity

1.  The resistance of an object depends on its _________________________ and the _______________ of which it is composed.

2.  R =

3.  Resistivity ρ is an ________________ _________________ of the material, independent of its shape or size.

4.  In home wiring, currents are limited and minimum wire thicknesses are specified because, as current and resistance increase, more _______________ is produced in the wires,

Notes – 20.4 Electric Power and Energy

5.  Power (P) is the ______________ of energy use or energy conversion.

6.  Voltage (electric potential) can be expressed as J/C, and Current (Amperes) can be

expressed as C/s.  Therefore, P= _______

7.  The unit for power is _________________.

8.  1 W = 1 ______________

9.  Given that V = IR, alternate expressions for power include:

P =

10.  The more electric appliances you use and the longer they are left on, the higher your electric bill.  This familiar fact is based on the relationship between energy and power. You pay for the _______________ used.

Notes – 21.1 Resistors in Series and Parallel

11.  Most circuits have more than one component, called a resistor that limits the flow of charge in the circuit.  A measure of this limit on charge flow is called ____________.

12.  Label which resistors are in series and which are in parallel.

_______________			        _______________

13.  Resistors in Series:

A.  Series resistances add.  Rseries = ____________________________

B.  The current flowing through resistors in series is

_________________________

C.  Individual resistors ____________ the overall voltage drop.

14.  Resistors in Parallel:

A.  Individual resistors’ voltages _______________________________________

B.  Resistors in parallel  ________________ the overall source current.

C.  Parallel resistances are found from ___________________________________

15.  Suppose the voltage output of a battery is 12.0 V, and the resistances for 3 resistors connected in series with the battery are R1 = 1.00 , R2 = 6.00  and R3 = 13.0 .

A.  Draw a diagram of the circuit.

B.  What is the total resistance?

C.  Find the current.

D.  Calculate the voltage drop in each resistor, and show these add to equal the voltage output of the source.

E.  Calculate the power dissipated by each resistor.

F.  Find the power output of the source, and show that it equals the total power dissipated by the resistors.

16.  Suppose the voltage output of a battery is 12.0 V, and the resistances for 3 resistors connected in parallel with the battery are R1 = 1.00 , R2 = 6.00  and R3 = 13.0 .

A.  Draw a diagram of the circuit.

B.  What is the total resistance?

C.  Find the total current.

D.  Calculate the currents in each resistor, and show these add to equal the total current output of the source.

E.  Calculate the power dissipated by each resistor.

F.  Find the power output of the source, and show that it equals the total power dissipated by the resistors.