Name:  ___________________________

Practice – 20.1 Current

1.  Car batteries are rated in ampere-hours (A ⋅ h).  To what physical quantity do ampere-hours correspond (voltage? Charge? Energy? . . .)?

2.  If two different wires having identical cross-sectional areas carry the same current, will the drift velocity be higher or lower in the better conductor?

3.  Why are two conducting paths from a voltage source to an electrical device needed to operate a device?

4.  Why isn’t a bird sitting on a high-voltage power line electrocuted?  Contrast this with the situation in which a large bird hits two wires simultaneously with its wings.

5.  What is the current in milliamperes produced by the solar cells of a pocket calculator through which 4.00 C of charge passes in 4.00 h?

6.  What is the current when a typical static charge of 0.250 μC moves from your finger to a metal doorknob in 1.00 μs?

7.  A large lightning bolt had a 20,000-A current and moved 30.0 C of charge.  What was its duration?

8.  A defibrillator passes 12.0 A of current through the torso of a person for 0.0100 s.  How much charge moves?

9.  A clock battery wears out after moving 10,000 C of charge through the clock at a rate of 0.500 mA.

A.  How long did the clock run?

B.  How many electrons per second flowed?

10.  A large cyclotron directs a beam of He++ nuclei onto a target with a beam current of 0.250 mA.

A.  How many He++ nuclei per second is this?

B.  How long does it take for 1.00 C to strike the target?

Solutions:

1.  charge	2. higher	3. a continuous path is needed

4. both feet are at the same potential

5.  0.278 mA		6.  0.250 A			7.  1.50 x 10-3 s		8.  0.120 C

9. A. 2.00 x 107 s       B. 3.13 x 1015 e-/s

10. A. 7.81 x 1014 He++/s       B. 4.00 x 103 s