Name:  ___________________________

Practice – 10.1 Angular Acceleration

1.  At its peak, a tornado is 60.0 m in diameter and carries 500 km/h winds.  What is its angular velocity in revolutions per second?

2.  An ultracentrifuge accelerates from rest to 100,000 rpm in 2.00 min.

A.  What is its angular acceleration in rad/s2?

B.  What is the tangential acceleration of a point 9.50 cm from the axis of rotation?

C.  What is the radial acceleration in m/s2 and multiples of g of this point at full rpm?

3.  A drum rotates around its central axis at an angular velocity of 12.60 rad/s.  If the drum then slows at a constant rate of 4.20 rad/s2,

A.  How much time does it take to come to a stop?

[Note:  f = 0 + t ]

B.  Through what angle does it rotate before coming to a stop?

[Note:  f – 0 = 0t + ½ t2 ]

4.  Starting from rest, a disk rotates about its central axis with constant angular acceleration.  In 5.0 s, it rotates 25 rad.  During that time, what is the magnitude of the angular acceleration?  [Note:  f – 0 = 0t + ½ t2 ]

Solutions:

1.  0.737 rev/s

2. A. 87.3 rad/s2 	B. 8.29 m/s2 	C. 1.04 x 107 m/s2,  1.06 x 106 g

3. A. 3.00 s		B. 18.9 rad

4.  2.0 rad/s2