Physics 200 (Stapleton) 				Name:  ___________________________

Practice – 16.10 & 17.5 Superposition, Interference and Resonance

1.  A “showy” custom-built car has two brass horns that are supposed to produce the same frequency but actually emit 263.8 and 264.5 Hz.  What beat frequency is produced?

2.  A piano tuner hears a beat every 2.00 s when listening to a 264.0-Hz tuning fork and a single piano string.  What are the two possible frequencies of the string?

3.  Another type of tube is one that is open at both ends.  Examples are some organ pipes, flutes, and oboes.  The resonances of tubes open at both ends can be analyzed in a very similar fashion to those for tubes closed at one end. The air columns in tubes open at both ends have maximum air displacements at both ends.  A standing wave occurs at resonance.

A.  What is the fundamental frequency of a 0.672-m-long tube, open at both ends, on a day when the speed of sound is 344 m/s?

B.  What is the frequency of its second harmonic?

4.  How long must an open-pipe (at both ends) instrument be in order to have a fundamental frequency of 262 Hz (this frequency corresponds to middle C on the evenly tempered chromatic scale) on a day when air temperature is 20.0ºC?

5. A.  Find the length of an organ pipe closed at one end that produces a fundamental frequency of 256 Hz when air temperature is 18.0ºC.

B.  What is its fundamental frequency at 25.0ºC?

Solutions:

1.  0.7 Hz            2.  263.5 Hz, 264.5 Hz            3. A. 256 Hz     B. 512 Hz         4.  0.655 m

5. A. 0.334 m      B. 259 Hz

Fret Distance Calculations for Your Instrument

| Your chosen distance from bridge to nut (inches) |  |
| --- | --- |
| Distance from bridge to nut (cm) |  |
| Wavelength of open string Fundamental (cm) |  |
| Frequency of Open String (hz) "open string" means the entire string oscillates. For calculations, we will assume that your open string produces an A at 440Hz | 440 |
| Speed of wave (inches/s) – constant for all calculations below |  |

Assuming that the wave speed for each of your strings remains constant at a given tension…

| half steps above open string | hz | wavelength | Vibrating string length (cm) | Distance of fret from nut (cm) |
| --- | --- | --- | --- | --- |
| 0 | 440 |  |  |  |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |
| 12 |  |  |  |  |